## Slide 1
COMSCI / ECON 206 | PS2 RESEARCH SYMPOSIUM | FALL 2026
FINAL POSTER · VALIDATED BASELINE
Share or Hide?
Strategic Disclosure in Congested Low-Altitude Drone Traffic
Yiqiao Liu · FP10
Course instructor: Professor Luyao Zhang
KEY MESSAGE
“The largest benchmark coordination failure appears at intermediate congestion, where additional disclosure is socially valuable but remains privately unattractive to confidentiality-sensitive operators.”
01 Question & model
Research question & verified gap
PRIMARY When operators privately differ in confidentiality cost, how does congestion affect strategic disclosure, and when does BNE fall below the full-information first best?
INTEGRATED How should low-altitude traffic systems structure non-safety sharing when confidentiality remains private but coordination is collective?
SETTING Capacity-constrained urban drone-delivery corridors. Stakeholders: operators, traffic authority, customers, nearby/public stakeholders, emergency users.
VERIFIED GAP Existing AAM work studies protocols, privacy mechanisms, and auctions. Here disclosure granularity is an endogenous choice under private commercial cost and congestion-dependent information value.
Strategic model & foundations
STATIC BAYESIAN GAME · INCOMPLETE INFORMATION
Players A, B. Private cᵢ ∈ {1, 1.6}; Pr(L)=Pr(H)=0.5. Public d: Low .3 | Medium .6 | High 1.0.
Actions: Minimum = mandatory/basic safety only; Partial = next sector + coarse ETA + traffic volume; Full = richer route/timing/trajectory.
Safety floor: Minimum never withholds required or safety-critical information.
uᵢ = dB[1−exp(−λ(xᵢ+xⱼ))] − cᵢk(aᵢ)
B=7.5; λ=.5; x=(0,1,2); k=(0,1,2.5). Solution: pure-strategy Bayesian Nash equilibrium.
Three complementary lenses
GAME THEORY Private types + M/P/F disclosure → Bayesian equilibrium
SOCIAL CHOICE BNE welfare vs full-information first best → efficiency and burden
MECHANISM DESIGN CCAR access rule + priority allocation → incentive robustness
Downstream Week 5 allocation application
Resource: one commercial priority slot, K=1; emergency/public-safety missions remain outside the auction.
Values A/B/C/D = 8/5/3/2; FCFS arrival B → C → A → D.
FCFS B wins | value 5 | efficiency 62.5%
SECOND PRICE A wins | payment 5 | utility 3 | efficiency 100%
Boundary: downstream scarcity allocation, not the disclosure mechanism.
02 Design & evidence
Figure 1. Economic model → verified computation → behavioral probe → bounded allocation → revision gate.
WHY MEDIUM? At high congestion, even the high-confidentiality type chooses Partial. At medium congestion, added disclosure is socially valuable but remains privately unattractive.
ROBUSTNESS 760 validated cells: 401 no equilibrium-set effect | 334 welfare improvement | 18 excessive-disclosure diagnostic | 3 larger gap | 66 multiple pure BNE | 0 no pure BNE. Categories overlap; these are not probabilities.
DESIGN MESSAGE Mechanism performance is parameter-dependent.
03 Impact & dialogue
Practical impact: a real-world case
CASE Commercial drone-delivery operators sharing capacity-constrained urban low-altitude corridors.
DECISION How much non-safety flight-intent information to share; how to allocate residual commercial priority scarcity.
POTENTIAL BENEFIT Better coordination, lower delay, more efficient corridor use.
RISKS Commercial confidentiality, unequal access, over-disclosure, misspecified incentives.
BEFORE ADOPTION Pilot calibration and confidentiality values; latency/reliability; safety and distributional review.
CORRECTION Auditable rule, safety-information floor, appeal/review, parameter revision, or suspension.
Interdisciplinary evidence
TESTABLE IMPLICATION
In an intermediate-congestion pilot with synthetic or calibrated confidentiality types, conditioning only enhanced non-safety coordination access on Partial/Full disclosure should increase Partial disclosure among confidentiality-sensitive operators relative to the baseline rule.
QUALIFY / REJECT IF disclosure becomes excessive; the welfare gap rises; access becomes systematically unequal; or operational/privacy costs dominate.
BEHAVIORAL SCIENCE Hugging Face Decision Lab: Solo Decision, reflection, Peer Play, benchmark reveal, CCAR comparison, auction exercise.
Evidence boundary: exploratory classroom decision exercise; not representative evidence about real drone operators.
COMPUTER SCIENCE GitHub + Colab 01 (BNE / welfare / CCAR) + Colab 02 (FCFS / second price).
Integration: the model defines the benchmark shown in the artifact; participant reflection identifies where predictions may require behavioral qualification.
Limitations & next test
LIMITS Two operators and types; independent private types; pure strategies; stylized parameters; no calibration; first best may be nonimplementable; CCAR cost omitted; IPV auction; interdependent mission values; exploratory demo.
NEXT TEST Compare baseline and CCAR under trusted-partner and competitive framing; classify deviations by privacy salience, reciprocity/fairness, or strategic misunderstanding.
REVIEWER QUESTION At what congestion and confidentiality conditions should enhanced access become conditional without creating excessive disclosure or unequal access?
PEER REVIEW: PARTIAL
Superseded-version review only; no final-topic review. Checkpoint: ffa4836208a3f647181771646c5639286c0726e6
Acknowledgments
Course instructor: Professor Luyao Zhang. No empirical operational dataset was used; inputs are stylized. Software: Python, NumPy, Matplotlib, nbclient, Gradio. Layout adapted from the official COMSCI/ECON 206 PS2 A0 Poster Template. Research question, model choices, interpretation, and final responsibility are the author’s. AI tools assisted implementation, debugging, literature-search support, reproducibility checking, formatting, and drafting/editing.
Selected references
Chin et al. (2023), Traffic Management Protocols for Advanced Air Mobility. Frontiers in Aerospace Engineering 2:1176969. doi:10.3389/fpace.2023.1176969
Maheshwari et al. (2025), Privacy-Preserving Mechanisms for Coordinating Airspace Usage in Advanced Air Mobility. ACM JATS 2(4). doi:10.1145/3732290
Raith (1996), A General Model of Information Sharing in Oligopoly. JET 71(1):260–288. doi:10.1006/jeth.1996.0117
Harsanyi (1967), Games with Incomplete Information Played by Bayesian Players I. Management Science 14(3):159–182. doi:10.1287/mnsc.14.3.159
Vickrey (1961), Counterspeculation, Auctions, and Competitive Sealed Tenders. Journal of Finance 16(1):8–37. doi:10.1111/j.1540-6261.1961.tb02789.x
OPEN MATERIALS
GitHub · code + reproducibility
HF · try the decision lab
Colab 01 · BNE / welfare / CCAR | Colab 02 · allocation
65 passed, 0 failed · hosted Run all confirmed
A0 landscape · 1189 × 841 mm · one editable slide · results from tracked outputs · peer review: PARTIAL (superseded version only)
STYLIZED
BENCHMARK
Private type +
public congestion
Choose
Minimum / Partial / Full
Compute
pure BNE
Compare welfare
with first best
Test CCAR
incentives
Decision Lab
Solo + Peer Play
Priority-slot
allocation
Robustness +
design implication
Largest benchmark welfare gap: MEDIUM congestion
CONGESTION | LOW TYPE | HIGH TYPE
LOW | Minimum | Minimum
MEDIUM | Partial | Minimum
HIGH | Partial | Partial
WELFARE GAP
LOW
0.639
MEDIUM
0.946
HIGH
0.503
Candidate mechanism: CCAR
Mandatory safety information remains universal. Only enhanced non-safety access changes.
BASELINE · MEDIUM
Low type: Partial
High type: Minimum
CCAR · αM = 0.7
Low type: Partial
High type: Partial
UNDERLYING WELFARE 2.193 → 3.089
GAP 0.946 → 0.050
Under the benchmark parameterization, CCAR moves the medium-congestion equilibrium closer to the full-information first best.
TRY THE
DECISION LAB
CODE +
REPRODUCIBILITY
Notes: Poster sources: outputs/tables/baseline_bne_summary.csv; baseline_welfare_gap.csv; ccar_bne_summary.csv; ccar_failure_regions.csv; auction_benchmark_example.csv.
Reproducibility checkpoint: ffa4836208a3f647181771646c5639286c0726e6.
Public artifacts: GitHub repository, Hugging Face Space, Colab 01 and Colab 02 as printed on the poster.
All inputs are stylized; no empirical operational or representative behavioral dataset is claimed.